## Slide 1: Chapter 12: Water Resources

## Slide 2: Water cycle

## Slide 3: Water cycle

## Slide 4: Water cycle

## Slide 5: Rainwater

## Slide 6: Surface Water
watershed - drainage basin
  https://www.epa.gov/waterdata/hows-my-waterway
supply factors
  precipitation
  geology
  basin shape, relief, slope, efficiency
  orientation to storms
  vegetation
  animals
  groundwater flow

## Slide 7: Surface Water

## Slide 8: Groundwater recharge
precipitation (ultimate source)
influent (losing) stream or lake

## Slide 9: Groundwater distribution
zone of aeration
water table
zone of saturation

## Slide 10: Groundwater distribution
zone of aeration
water table
zone of saturation
aquifer
  unconfined
  confined
  perched
  artesian
aquitard/aquiclude

## Slide 13: groundwater discharge
effluent stream
  gains water
  base flow
spring
well

## Slide 14: Groundwater Flow
  Darcy’s law Q=KiA
    Q = discharge (volume/time)
    K = hydraulic conductivity
      permeability
      porosity
    i = hydraulic gradient = h/l
      h = change in water table elevation
      l = distance between wells
    A = x-sectional area
  rate of flow - cm/day (at best)
    V = Ki
  residence time
    1000s to 10,000s of years

## Slide 15: Groundwater Flow
Q = KiA
V = Ki

## Slide 16: Wells
cone of depression

## Slide 17: Wells
cone of depression
artesian wells
yield
  sustainable
  mining

## Slide 19: groundwater-surface water interaction
gaining and losing streams
springs

## Slide 20: groundwater-surface water interaction
gaining and losing streams
springs
karst
  sinkholes
  disappearing streams

## Slide 21: groundwater-surface water interaction

## Slide 23: Water supply
Water budget
  Input (rain\run on)
  output
    runoff
    withdrawal
    subsurface flow
    evaporation
    transpiration
flood vs drought
  https://www.drought.gov

## Slide 24: Water Use in the U.S.
Estimated Use of Water in the United States in 2015
  https://pubs.er.usgs.gov/publication/cir1441

## Slide 25: Water Use in the U.S.

## Slide 26: Water Use in the U.S.

## Slide 30: Surface Water Use
in-stream use
  navigation
  power
  habitat
  recreation
off-stream
  agricultural
  residential - (inc. drinking)
  industrial & commercial
  municipal

## Slide 31: Water management
supply vs demand
  volume over time
  overdraft
develop supplies
  wells
  reservoirs
  aqueducts
reallocation of use
conservation
increase efficiency
recycling of waste water

## Slide 32: Water use issues
out of basin use
consumptive use
sewage
sedimentation

## Slide 33: surface water rights
riparian
  adjacent landowner
  goes with property
  east of Miss
prior appropriation
  volume per year
  separate from other property rights
  west of Miss

## Slide 34: groundwater rights
absolute ownership (pump at will)
  reasonable use
  correlative rights
  all owners =
  safe yield is divided
prior appropriation